## Slide 1: CS 2600 Computer Networks I Dr. Sayeed Sajal Lecture 25 Virtual Circuit Networks

## Slide 2: The Three Phases of a Virtual Circuit
Establish the connection/virtual circuit
  Connection request allows discovery of the best path across the network
  Also allows the destination host to accept or reject the request
  May be a short-term switched or a long-term permanent virtual circuit
2. Hold the conversation
  All traffic follows the same pre-established path
3. Terminate the connection/virtual circuit

## Slide 3: Switching a Data Packet From Host A to Host B (Based on text pp. 176 - 179)
After a virtual circuit is established, each switch contains a Virtual Circuit Table which maps the Virtual Circuit Identifier (VCI) in the header of a packet received on an interface to an outbound interface and a new VCI. A VCI is only significant on a certain switch and interface, so the overall virtual circuit consists of a chain of VCI’s (in this example 5, 11, 7, 4). As the packet flows through each switch, the incoming VCI is removed from the packet header and replaced with the outgoing VCI.
Figure 3.5 A packet makes its way through a virtual circuit network.
5
11
7
4
VCI
(partial)
(partial)
Packet Flow

## Slide 4: Characteristics of Virtual Circuit Protocols
Sometimes called “reliable”, because prior to data transmission…
  Existence of path is confirmed
  Destination host has approved the connection
However, data can’t be transmitted until a “Connection Accepted” packet is received back from the destination host
  So there’s a minimum of 1 RTT of delay for a new connection
  Bad for short transactions
If a switch or link fails, all virtual circuits using that resource are lost
  User is usually alerted to the failure, but…
  Each virtual circuit must be reestablished

## Slide 5: The Frame Relay PDU*
*“Protocol Data Unit”, an intentionally ambiguous term used in some European-influenced
standards to mean “A message that we don’t want to associate with a specific layer.”
Thus it can’t be called a “frame”, “packet” or whatever. A Frame Relay PDU combines
OSI layer 2 and 3 functions. (A more descriptive term for a Frame Relay PDU that also
pays homage to Battlestar Galactica might be “fracket”.)

## Slide 6: Slide 6
Quality of Service (QoS) is a term associated with networks that can transport traffic with special requirements (such as voice or video). QoS may include a guaranteed data rate, as well as possible limits on latency, packet loss and jitter. Frame Relay and ATM networks have QoS capabilities.

## Slide 7: Three Generations of Virtual Circuit Connection-Oriented Packet Switching Standards
Service | Data Rate | Reliable? | QoS? | Current Status
X.25 (1976–2006) | 9600bps - 64Kbps | Yes | No | Mostly obsolete
Frame Relay (1990–present) | 56Kbps - 45Mbps | No | Data rate only | In decline
ATM (WAN) (1995–present) | 1Mbps - 599 Mbps (OC12)* | No | Data rate, latency, frame loss | Common (WANs), declining (LANs)
*Bell South MSATMS - wholesale.att.com/products_and_services/access/data/msatm.html

## Slide 8: ATM Quality of Service (QoS) Options
Constant Bit Rate (CBR)
  Highest priority service option
  Guaranteed cell (fixed-length frame) rate, maximum delay and cell loss
  Originally designed for voice traffic (competes with SONET)
Variable Bit Rate (VBR)
  Used to multiplex voice and data over a single virtual circuit
  Also makes guarantees about cell loss and delay
Available Bit Rate (ABR)
  Lower cost than CBR or VBR, but…
  Significant cell loss and delay may occur if VBR users saturate switches with transmission bursts
  Designed for interconnecting LANs at remote locations
Unspecified Bit Rate (UBR)
  Lowest priority service option
  No QoS guarantees
  Used by applications that aren’t delay-sensitive and can manage cell loss
  on their own (email, file transfer, web, anything that runs over TCP)

## Slide 9: Queue Behavior with 4K Byte Packets

## Slide 10: Queue Behavior with 53 Byte Cells

## Slide 11: The Sixth Principle of Network Design
“Compared with large variable-length packets, using small fixed-length cells improves control over the queues in switches.”
Why? Using small fixed-length cells minimizes switching (queuing) delay for the higher priority cells, and using fixed length cells makes that delay more predictable.

## Slide 12: Network Jitter
A jitter buffer that compensates for jitter. The buffer holds K time units of data.
(whenever they arrive)

## Slide 13: ATM Cell Format* (Based on text Fig. 3.6)
*A cell is a fixed length frame. Note that there is no frame number in the ATM cell header, and therefore no ACK/NAK or retransmission capability in ATM.

## Slide 14: Relationship Between Virtual Circuits and Virtual Paths