## Slide 1: CS 2600 Computer Networks I Dr. Sayeed Sajal Lecture 6 Network Performance

## Slide 2: Bandwidth ≈ Throughput ≈ Data Rate
Bandwidth, throughput and data rate usually refer to the number of bits that can be transmitted onto (or received off of) a link in some unit of time
Typically measured in bits per second (bps) on networks, but bytes per second (Bps) on a computer’s internal system bus
  For example 1,000,000bps = 1Mbps = 125,000Bps = 125KBps
Bandwidth is the most commonly used term
  But perhaps not the best choice, since bandwidth has a different meaning in the analog world (for example, to an electrical engineer)
Throughput is useful, because it has the connotation of “flow”, and sometimes refers to how much “actual” data is communicated on a continuous basis
Data rate is probably most descriptive for computer scientists, as long as we think of “data” as the number of bits that are transmitted/received per unit of time (measured as an instantaneous rate)
Computer scientists tend to use all three terms interchangeably
  Electrical engineers and techs don’t
In this class, all three terms mean the same thing unless we’re discussing analog transmission systems (more on that later)

## Slide 3: Small Units of Time
  millisecond (ms) - one thousandth of a second (0.001 or 10-3 sec.)
  Typical units for wide area networks
  microsecond (µs) - one millionth of a second (0.000001 or 10-6 sec.)
  Typical for LANs
  The Greek “µ” (Mu) character connotes “million”
  nanosecond (ns) - one billionth of a second (10-9 sec.)
  Typical for processing inside the computer
  picosecond (ps) - one trillionth of a second (10-12 sec.)
Example: at 1Mbps, a DSL link takes 1µs (microsecond) to transmit one bit
Data rate = 106bps
Time to transfer 1 bit = 1 = 10-6 bps = .000001s = 1µs
data rate

## Slide 4: Serial vs. Parallel Communication
Serial communication systems transmit bits one-by-one
  Like a one lane road
  Most computer networks work this way
Parallel communication systems transmit bits in groups, normally 1, 2 or 4 bytes at a time
  Like a freeway with many lanes
  This is how data is transmitted over the system bus inside of many computers*
  These computers use parallel transmission internally because the system bus can put each bit from a 2, 4 or 8-byte group on a different bus circuit, and then transmit them all simultaneously
  To convert bits per second (bps) to bytes per second (Bps), divide by 8
On a network, we are usually limited to a single circuit (or fiber, or radio frequency), so we are typically restricted to serial transmission
  All else being equal, serial communication will be slower
  Some network links can use limited parallel transmission (2, 3 or 4 bits at a time) using technologies like QAM, WDM or MIMO
  *The PCI Express (PCIe) bus is fast serial bus

## Slide 5: Animations of Serial and Parallel Communication
Serial Transmission
Parallel Transmission

## Slide 6: Figure 1.16 Bits Transmitted at a Particular Bandwidth Can Be Regarded as Having Some Width…
Volts
Volts
1-bit
0-bit
Elapsed time =

## Slide 7: Factors That Affect Frame Transmission Time*
*Assumes serial “one-bit-at-a-time” transmission

## Slide 8: Latency = Delay ≈ Propagation Time
Latency, delay and propagation time are terms that generally refer to the amount of time it takes a single bit to cross a link or an entire network
Think of this as “travel time” – the longer the distance, the longer the latency
The type of media is also a factor
  For example, radio signals travel about 50% faster than signals on wire
  However, type of media is usually not much of a variable, compared to distance (i.e., distance dominates the calculation)
If we’re talking about latency over a network, then the processing speed of switches, routers and servers adds additional delay
  Technically that is considered queuing delay (see next slide)
  In some cases, we may just lump these two types of delay together and consider switch-based delay part of the latency of the link
So we use the term propagation time or propagation delay when we are referring to travel time across a single link (as opposed to an entire network or internet)
Two-way latency is called round trip time (RTT)

## Slide 9: Queuing Delay
Queuing delay is the time that a frame or packet spends in a computer, either being processed or waiting (in a queue) for processing
On a network or internet connection, queuing delay occurs in switches and routers along the path between source and destination
It also occurs in the destination host
  For example, when a slow or overloaded web server processes your browser’s request for a web page
There is also queuing delay back at the source, as the client processes the returning message or renders it for display
Obviously, if we are to solve the problem of a “slow network”, we must be able to identify which element(s) in the system is causing significant delay – in other words “where’s the bottleneck?” Often, it isn’t the network.

## Slide 10: Relationships That Affect Total Latency Over a Single Link*
Total Latency = Propagation Time + Transmission Time + Queuing Time
Propagation time (time to travel across the media)  Distance___
Speed of medium
Transmission time (time to send the data “out the door”)  Message size
Data rate
Queuing time (time required for switches/routers/hosts to process the
frames/packets)  Amount of competing traffic
Processing power of nodes
  *For additional help with bandwidth vs. latency concepts check out Bill Marek’s excellent tutorial on this topic in the Canvas folder Files/Tutorials/Network Performance/index.html

## Slide 11: Calculating Total Latency (RTT) on a Single Link Using a Vertical Time Line

## Slide 12: Figure 1.18 Network as a Pipe
Delay x Bandwidth = the “Volume” of the pipe

## Slide 13: Calculation of Pipe Volume (Based on text p. 49)
A transcontinental channel has a one-way propagation time of 50ms (0.05 seconds)*
The data rate is 45Mbps
The volume of bits that the pipe can hold is equal to
.05 sec. x (45 x 106) bps
= 2,250,000 bits
= 2.25Mb
≈ 280KB (divide by 8)
(Note the conversion from bits (b) to bytes (B), and how seconds “cancel out”)
*Approximate propagation time for a U.S. coast to coast fiber optic link

## Slide 14: Two Ways to Count Bits

## Slide 15: Quiz Next Time
Covers from pp. 24 – 58 in the text (Lectures 4 - 6), which includes network architecture concepts; both the OSI and the Internet models; the standards development processes, related terminology and the organizations involved; and the discussion of bandwidth vs. latency.

## Slide 16: Homework Question C.
  This set of homework questions will be submitted to Canvas and graded. They are due before the start of the next lecture. No credit for late or paper submissions. You must show your work on all calculations.
  For additional help with bandwidth vs. latency concepts check out Bill Marek’s tutorial on this topic in the Canvas folder Files/Tutorials & Guides/Network Performance/index.html. Make sure you have an accurate PowerPoint viewer. (108 ≠ 108!)
C. How much time does it take to transmit one bit on a 1-Gbps link? (Assume 1G = 109.) To receive credit, you must show your work on all calculations.
How long (in meters) is that same bit when transmitted over a copper wire, where the propagation velocity is 2.3 x 108 meters per second? (In other words, how far does the leading edge of this bit travel down the wire during the transmission time calculated in the previous step.) (3 points)

## Slide 17: Homework Question 12.
12. How long does it take to transmit an x-KB file over a y-Mbps link? Give your answer as a ratio of x and y. (Assume 1K = 103 and 1M = 106, and think of the entire file as a single message). (2 points)

## Slide 18: Homework Question 13.
13. Suppose a 1Gbps point-to-point link is being set up between the Earth and a new lunar colony. The distance from the moon to Earth is approximately 385,000 km, and data travels over the link at the speed of light (3 x 108 meters per sec.). (5 points)
(a) Calculate the minimum RTT (two-way propagation time) for the link. (In other words, how long would it take to send a single bit to the moon and immediately bounce it right back to Earth?)
(b) Using the RTT as the delay, calculate the delay x bandwidth product for the link.
(c) What is the significance of the delay x bandwidth product computed in (b)?
(d) A camera on the lunar base takes pictures of the Earth and saves them in digital format to disk. Suppose Mission Control on Earth wishes to download the most current image, which is 25MB. What is the minimum amount of time that will elapse between when the request for the data goes out and the transfer is finished?

## Slide 19: (End of Chapter 1 Slides)